Basic working of MAX30100 sensor

-- The MAX30100 is an is an optical sensor that measures heartbeat and blood oxygen saturation (SpO2) using light.
It has two led’s -- 1) Red light
     2) Infrared light
-- It also has one photodetector which detects and convert light ( or electromagnetic radiation) into an electrical signal.

Working :
1. Light absorption :
After powering ON MAX30100 turns ON either RED led and Infrared led or both. The light penetrates into the skin and blood vessels.

2. Light absorption :
When light penetrates the skin Oxygeneted (blood loaded with oxygen) and deoxygeneted (blood lacking oxygen) blood absorb Red and IR light differently. As heart beats, blood volume in the finger changes causing the amount of absorbed / reflected light to vary over time. Oxygeneted blood absorbs more infrared light and allows more red light to pass through. Deoxygenated blood allows more infrared light to pass through and absorbs more red light.

3. Light Detection
The photodetedtor collects light which reflected from blood vessels. This reflected light generates a small electrical signal which is proportional to how much light is received.

4. Signal conversion
The MAX30100 has a analog to digital converter (ADC) inside. Using this ADC the small electrical signals which are generated from photodetector are digitized into 16 bit digital values.

5. Data Readout (I2C)
We read the IR value and Red valur through the I2C bus. Each reading tells how much light was detected after passing through blood.

Heart Rate Measurement Algorithm

Input : -
IR samples from MAX30100

1. Initialize MAX30100 :
-- Set MAX30100 sensor to Heart Rate mode or SpO2 mode i.e. bothe LED’s ON.
-- Set sample rate (e.g. 100 Hz)
-- Set appropriate LED current.
2. Continuously read IR values
-- Fetch IR value from FIFO register
3. Filter the IR signal
-- Apply a moving average filter or low pass filter to reduce noise.

4. Detect peaks
-- Compare each sample with neighbors (simple peak detection).

5. Measure time between peaks
-- Store timestamp (in milliseconds) of each detected peak.
-- Calculate difference between consecutive peaks.

6. Calculate Heart Rate (BPM)
-- Heart Rate (BPM) = 60000 / interval (if interval is in milliseconds)
-- atke average over last few intervals for better stability.

SpO2 Measurement Algorithm

Input : -
IR and Red samples from MAX30100

1. Initialize MAX30100
-- Set MAX30100 to SpO2 mode (Red + IR LED’s ON).

2. Continuously read IR and Red values
-- Fetch both IR and Red from FIFO.

3. Calculate DC and AC components
-- DC = moving average of the signal (baseline).
-- AC = peak-to-peak amplitude after subtracting DC.

4. Calculate ratio (R)
-- Using : R= (AC red / DC red) / (AC ir / DC ir)

5. Estimate SpO2
-- Apply calibration formula :
SpO2 = 110 - 25 * R;
-- (Constants 110 and 25 vary depending on calibration – these are typical values).